## Slide 1
GROUP 7
COE 381 — Microprocessors
KNUST | Dept. of Computer Engineering
GROUP MEMBERS
1. Asiedu Seth Osei
2. Frimpong Roddy
3. Jessica Oforiwaa Anim
4. Asante Samuel Osei
5. Bosomtwi Akosua Serwaa Maame
6. Daniel Kuma Gyebi
7. Samuella Andoh Bannerman
8. Kamil Khadija Ndaiya
9. Frimpong Solomon Junior
High-Precision
Dual-Player Reaction Time
Measurement System
Using ESP32 Microcontroller + Wokwi Simulation
Supervisor
Dr. Eliel Keelson
Deadline
March 29, 2026
Platform
Wokwi + ESP32
"How fast is your reaction? We built a system to prove it."

## Slide 2
Table of Contents
COE 381 | Group 7 | KNUST
Dual-Player Reaction Time System | Slide 2 of 11 | March 2026
What We Will Cover Today
01
Problem Statement
What problem we are solving and why it matters
02
Methodology
Hardware design, firmware logic, FSM architecture
03
Code Walkthrough
ISRs, buzzer functions, and FSM switch-case
04
Live Simulation Demo
Wokwi running — normal rounds, false starts, scores
05
Results & Findings
Reaction time data and system performance
06
Conclusion
Achievements, challenges, and future improvements

## Slide 3
Problem Statement
COE 381 | Group 7 | KNUST
Dual-Player Reaction Time System | Slide 3 of 11 | March 2026
"Have you ever argued with a friend about who reacted faster? How would you actually prove it?"
Expensive & Opaque
Commercial reaction time systems cost hundreds of dollars and hide all engineering detail from the user. They give results without explaining how.
Single-Player Only
Existing educational prototypes are single-player. They cannot support competitive two-player comparison or demonstrate concurrent interrupt handling.
No Educational Value
Neither option demonstrates embedded systems concepts — GPIO interrupts, FSM design, I2C communication, or real-time timing logic — to engineering students.
Our Solution: A dual-player ESP32-based system that measures reaction times with millisecond precision — open, educational, and competitive.

## Slide 4
System Architecture & Components
COE 381 | Group 7 | KNUST
Dual-Player Reaction Time System | Slide 4 of 11 | March 2026
How the System Works — End to End
INPUT
Stimulus LED
(GPIO 15)
Player 1 Button
(GPIO 4)
Player 2 Button
(GPIO 5)
PROCESSING
ESP32 MCU
240MHz Dual-Core
FSM Firmware
5 States
millis() Timer
ms Precision
OUTPUT
16x2 LCD Display
I2C (GPIO 21/22)
Passive Buzzer
(GPIO 18)
Serial Monitor
Debug Output
→
→
GPIO 15 → LED | GPIO 4 → P1 Button | GPIO 5 → P2 Button | GPIO 18 → Buzzer | GPIO 21/22 → LCD I2C

## Slide 5
Methodology — Hardware Design
COE 381 | Group 7 | KNUST
Dual-Player Reaction Time System | Slide 5 of 11 | March 2026
Circuit Design
Stimulus LED
GPIO 15 → 220Ω resistor → LED anode
R = (3.3V − 2.0V) / 0.010A = 130Ω → use 220Ω
Player Buttons
GPIO 4 & 5 with INPUT_PULLUP
Active-low: pressed = LOW, released = HIGH
Buzzer
GPIO 18 direct drive
digitalWrite HIGH = sound, LOW = silent
LCD I2C
SDA → GPIO 21, SCL → GPIO 22
Address 0x27, 16 cols × 2 rows

## Slide 6
Methodology — Firmware & FSM Design
COE 381 | Group 7 | KNUST
Dual-Player Reaction Time System | Slide 6 of 11 | March 2026
5-State Finite State Machine
IDLE
Waiting
to Start
→
WAITING
Random
Delay
→
↓ False Start
STIMULUS
LED ON
GO Signal
→
RESULT
Show
Results
FAULT
False
Start!
← Returns to WAITING after result or fault
volatile keyword
Shared ISR variables — prevents compiler caching stale values
IRAM_ATTR
ISRs stored in fast RAM — eliminates flash cache latency
FALLING edge
Interrupts fire when button pin goes HIGH → LOW on press
millis() Timer
Records ms since power-on — reaction = press time − LED time
gameActive flag
Gate that allows ISR recording only during stimulus phase

## Slide 7
Code Walkthrough — Key Sections
COE 381 | Group 7 | KNUST
Dual-Player Reaction Time System | Slide 7 of 11 | March 2026
The Most Important Parts of reaction_time_game.ino
Interrupt Service Routine
void IRAM_ATTR player1ISR() {
if (gameActive && !p1Pressed) {
p1Pressed = true;
p1Time = millis();
}
}
Reaction Time Calculation
stimulusBeep();
digitalWrite(LED_PIN, HIGH);
gameActive = true;
stimulusTime = millis();
p1Reaction = p1Time - stimulusTime;
p2Reaction = p2Time - stimulusTime;
IRAM_ATTR
Runs ISR from fast internal RAM — not flash. Saves ~200ns per call.
gameActive gate
Only records presses when LED is ON. Prevents false recordings.
volatile flag
p1Pressed is volatile — compiler always reads fresh value from memory.
Ternary timing
p1Reaction = p1Pressed ? (p1Time - stimulusTime) : 0

## Slide 8
Buzzer Feedback System — Audio Intelligence
COE 381 | Group 7 | KNUST
Dual-Player Reaction Time System | Slide 8 of 11 | March 2026
Every Game Event Has a Unique Sound Pattern
System Startup
1 short beep
Duration: 150ms
When ESP32 powers on
Round Starting
2 quick soft beeps
Duration: 60ms x2
After button starts a round
LED Stimulus — GO!
3 sharp beeps
Duration: 100ms x3
When LED activates — REACT NOW
Winner!
1 long celebratory beep
Duration: 600ms
Valid press detected, winner declared
Draw Result
4 rapid alternating beeps
Duration: 80ms x4
Equal reaction times detected
FALSE START
1 very long alarm tone
Duration: 1200ms
Button pressed during WAITING phase

## Slide 9
Live Simulation Demonstration — Wokwi
COE 381 | Group 7 | KNUST
Dual-Player Reaction Time System | Slide 9 of 11 | March 2026
Watch the System Run — Live on Screen
01
System Boots Up
LCD shows GROUP 7 GAME. Startup beep fires. Press any button to start.
02
WAIT FOR IT Phase
Random 2–5 second delay begins. LCD shows WAIT FOR IT. Watching for false starts.
03
GO Signal — LED Fires
LED turns ON. 3 sharp buzzer beeps. PRESS NOW on LCD. Both ISRs now active.
04
Players React
Both buttons clicked. p1Time and p2Time recorded by ISRs instantly.
05
Results Displayed
LCD: P1: 245ms P2: 312ms. P1 WINS declared. Winner beep fires.
06
False Start Test
Click a button during WAIT FOR IT phase. FALSE START shown. 1200ms alarm beep.

## Slide 10
Results & Discussion
COE 381 | Group 7 | KNUST
Dual-Player Reaction Time System | Slide 10 of 11 | March 2026
What Our System Achieved
Round | P1 Time | P2 Time | Winner | Notes
1 | 339ms | 320ms | P2 | Normal round
2 | 320ms | 320ms | Draw | Normal round
3 | No Response | No Response | Void | Void round
4 | FALSE START | — | FAULT | P1 pressed early
5 | — | FALSE START | FAULT | P2 pressed early
Key Findings
Millisecond timing worked correctly in all rounds
False start detection triggered 100% of the time
Winner arbitration correct for all test scenarios
LCD updated within 100ms of round completion
±5ms browser simulation variance noted vs real hardware
Innovation: Dual-player concurrent ISR management, randomised RNG delay, false-start FSM logic, multi-event buzzer patterns, and gameActive gating — all on a single ESP32 chip.

## Slide 11
Conclusion
COE 381 | Group 7 | KNUST
Dual-Player Reaction Time System | Slide 11 of 11 | March 2026
What We Achieved
• Dual-player reaction time measured in milliseconds
• 5-state FSM running flawlessly in Wokwi
• False start detection — 100% reliable
• Multi-event buzzer feedback system
• Complete I2C LCD interface
• Full academic documentation suite
Challenges We Overcame
• Understanding volatile and ISR safety
• LCD I2C address configuration (0x27)
• Button debounce in simulation
• Concurrent dual-ISR timestamp logic
• FSM return vs break distinction
Future Improvements
• Physical ESP32-S3 + SPI TFT display
• EEPROM session data logging
• WiFi score transmission dashboard
• Hardware RC debounce circuits
• Auditory stimulus mode
• Multi-round tournament scoring
"This project demonstrates that complex embedded systems — real-time interrupts, FSM design, and multi-peripheral control — can be built, understood, and explained by students from the ground up."